# RZ 314 CG-S

Pos. ...)  ... pcs.

Exit Luminaire acc. EN 60598-1, EN 60598-2-22 and EN 1838.

ARC-luminaire with variable perforated plate surface and special designed finish body of luminaire with EVG (automatic cut-off for failures within the lamp circuit).

EVG with ENEC-test mark, certified from an independent testing lab, with integrated monitoring facility. Allows single luminaire monitoring with address-switches for 20 addresses.

Switching modes (maintained/non-maintained and switched emergency luminaries) freely programmable with suitable emergency lighting systems. Mixed operation possible in a single circuit.

Marking: Silk-screened legend

Viewing distance: 18 m

Voltage range: 230 V 50/60 Hz, 220 V DC +25/-20%

Current drawn (battery operation): 20 mA

Power consumption: 10 VA

Permissible temperature range: -10°C up to +40°C

Loop terminals: 3 x 2.5 sqmm

Insulation class: I, Degree of protection: IP 20

Inclusive lamp: 4 W T16

Dimensions (mm): L = 220, H = 110, D = 70

Colour of enclosure:

- White

- Chrome

- Gold

Type: RZ 314 CG-S

Manufactured by: CEAG

# RZ 324 CG-S

Pos. ...)  ... pcs.

Exit Luminaire acc. EN 60598-1, EN 60598-2-22 and EN 1838.

ARC-luminaire with variable perforated plate surface and special designed finish with EVG (automatic cut-off for failures within the lamp circuit). Luminaire with double sided light outlet and exit-legends.

EVG with ENEC-test mark, certified from an independent testing lab, with integrated monitoring facility. Allows single luminaire monitoring with address-switches for 20 addresses.

Switching modes (maintained/non-maintained and switched emergency luminaries) freely programmable with suitable emergency lighting systems. Mixed operation possible in a single circuit.

Marking: Silk-screened legend

Viewing distance: 18 m

Voltage range: 230 V 50/60 Hz, 220 V DC  +25/-20%

Current drawn (battery operation): 20 mA

Power consumption: 10 VA

Permissible temperature range: -10°C up to +40°C

Loop terminals: 3 x 2.5 sqmm

Insulation class: I, Degree of protection: IP 20

Inclusive lamp: 4 W T16

Dimensions (mm): L = 220, H = 110, D = 85

With single pendulum 0.5 m and wall bracket/termination box

Colour of enclosure:

- White

- Chrome

- Gold

Type: RZ 324 CG-S

Manufactured by: CEAG