SpiritLED 28 – for recessed ceiling mounting with wire suspension

Pos. ...)  ... pcs.

LED – exit sign luminaire according to DIN EN 60598-1, DIN EN 60598-2-22 and DIN EN 1838

Exclusive exit sign luminaire with LED technology with recessed ceiling mounting kit for wire suspension. Frameless optic due to in acrylic integrated legends with LED-module. Uniform illumination of the pictogram by special lightguide technology (Lmin/max >= 0,5).

Recessed ceiling mounting kit with transparent isolated wire suspension for voltage supply, chrome plated ceiling duct and plastic housing for the LED converter with strain reliefs for mains and LED-supply.

Special LED-Converter with integrated monitoring module for individual monitoring of luminaries (monitoring of the supply and automatic detection of faulty supply of the LED-module).

Switching mode (non-maintained mode, maintained mode or switching maintained mode)

is free programmable with capable emergency lighting systems.

Different switching modes in one circuit are possible.

Marking: Silk-screened legend

Viewing distance: 28m

With variable wire suspension, max. 1m

Voltage range: 230 V/240V 50/60Hz, 220V DC +25/-20%

Current consumption (battery operation): 27 mA

Power consumption: 8,7 VA

Permissible temperature range: -10 °C to +40 °C

Loop terminals: 2 x 2,5 sqmm

Insulation class: I

Degree of protection: 	Panel 			IP 41

Converter housing	IP 30

Inclusive LED module with 36 white high brightness LEDs.

Dimensions panel (mm): 		W = 330; H = 208; T = 20

Dimensions converter housing (mm): 	W = 290; H = 33; T = 50

Type: SpiritLED 28 – for recessed ceiling mounting with wire suspension

Manufactured by: CEAG

SpiritLED 28  – for surface ceiling mounting or wall parallel mounting with wire suspension

Pos. ...)  ... pcs.

LED – exit sign luminaire according to DIN EN 60598-1, DIN EN 60598-2-22 and DIN EN 1838

Exclusive exit sign luminaire with LED technology with surface mounting kit for wire suspension. Frameless optic due to in acrylic integrated legends with LED-module. Uniform illumination of the pictogram by special lightguide technology (Lmin/max >= 0,5).

Surface mounting kit for ceiling mounting or wall parallel mounting including transparent isolated wire suspension for voltage supply and aluminium coloured canopy.

Special LED-Converter with integrated monitoring module for individual monitoring of luminaries (monitoring of the supply and automatic detection of faulty supply of the LED-module).

Switching mode (non-maintained mode, maintained mode or switching maintained mode)

is free programmable with capable emergency lighting systems. Different switching modes in one circuit are possible.

Marking: Silk-screened legend

Viewing distance: 28m

With variable wire suspension, max. 1m

Voltage range: 230 V/240V 50/60Hz, 220V DC +25/-20%

Current consumption (battery operation): 27 mA

Power consumption: 8,7 VA

Permissible temperature range: -10 °C to +40 °C

Loop terminals: 2 x 2,5 sqmm

Insulation class: I

Degree of protection: IP 41

Inclusive LED module with 36 white high brightness LEDs.

Dimensions panel (mm): 		W = 330; H = 208; T = 20

Dimensions canopy (mm): 		W = 330; H = 39; T = 46

Type: SpiritLED 28 – for surface ceiling mounting or wall parallel mounting with wire suspension

Manufactured by: CEAG

SpiritLED 28  – for surface ceiling mounting or wall mounting

Pos. ...)  ... pcs.

LED – exit sign luminaire according to DIN EN 60598-1, DIN EN 60598-2-22 and DIN EN 1838

Exclusive exit sign luminaire with LED technology with surface mounting kit. Frameless optic due to in acrylic integrated legends with LED-module. Uniform illumination of the pictogram by special lightguide technology (Lmin/max >= 0,5).

Surface mounting kit for ceiling mounting or 90° rotated wall mounting including with aluminium coloured canopy.

Special LED-Converter with integrated monitoring module for individual monitoring of luminaries (monitoring of the supply and automatic detection of faulty supply of the LED-module).

Switching mode (non-maintained mode, maintained mode or switching maintained mode)

is free programmable with capable emergency lighting systems. Different switching modes in one circuit are possible.

Marking: Silk-screened legend

Viewing distance: 28m

Voltage range: 230 V/240V 50/60Hz, 220V DC +25/-20%

Current consumption (battery operation): 27 mA

Power consumption: 8,7 VA

Permissible temperature range: -10 °C to +40 °C

Loop terminals: 2 x 2,5 sqmm

Insulation class: I

Degree of protection: IP 41

Inclusive LED module with 36 white high brightness LEDs.

Dimensions panel (mm): 		W = 330; H = 208; T = 20

Dimensions canopy (mm): 		W = 330; H = 39; T = 46

Type: SpiritLED 28  – for surface ceiling mounting or wall parallel mounting with wire suspension

Manufactured by: CEAG

SpiritLED 16 – for recessed ceiling mounting with wire suspension

Pos. ...)  ... pcs.

LED – exit sign luminaire according to DIN EN 60598-1, DIN EN 60598-2-22 and DIN EN 1838

Exclusive exit sign luminaire with LED technology with recessed ceiling mounting kit for wire suspension. Frameless optic due to in acrylic integrated legends with LED-module. Uniform illumination of the pictogram by special lightguide technology (Lmin/max >= 0,5).

Recessed ceiling mounting kit with transparent isolated wire suspension for voltage supply, chrome plated ceiling duct and plastic housing for the LED converter with strain reliefs for mains and LED-supply.

Special LED-Converter with integrated monitoring module for individual monitoring of luminaries (monitoring of the supply and automatic detection of faulty supply of the LED-module).

Switching mode (non-maintained mode, maintained mode or switching maintained mode)

is free programmable with capable emergency lighting systems.

Different switching modes in one circuit are possible.

Marking: Silk-screened legend

Viewing distance: 28m

With variable wire suspension, max. 1m

Voltage range: 230 V/240V 50/60Hz, 220V DC +25/-20%

Current consumption (battery operation): 22 mA

Power consumption: 5,0 VA

Permissible temperature range: -10 °C to +40 °C

Loop terminals: 2 x 2,5 sqmm

Insulation class: I

Degree of protection: 	Panel 			IP 41

Converter housing	IP 30

Inclusive LED module with 18 white high brightness LEDs.

Dimensions panel (mm): 		W = 200; H = 135; T = 20

Dimensions converter housing (mm): 	W = 290; H = 33; T = 50

Type: SpiritLED 16 – for recessed ceiling mounting with wire suspension

Manufactured by: CEAG

SpiritLED 16  – for surface ceiling mounting or wall parallel mounting with wire suspension

Pos. ...)  ... pcs.

LED – exit sign luminaire according to DIN EN 60598-1, DIN EN 60598-2-22 and DIN EN 1838

Exclusive exit sign luminaire with LED technology with surface mounting kit for wire suspension. Frameless optic due to in acrylic integrated legends with LED-module. Uniform illumination of the pictogram by special lightguide technology (Lmin/max >= 0,5).

Surface mounting kit for ceiling mounting or wall parallel mounting including with transparent isolated wire suspension for voltage supply and aluminium coloured canopy.

Special LED-Converter with integrated monitoring module for individual monitoring of luminaries (monitoring of the supply and automatic detection of faulty supply of the LED-module).

Switching mode (non-maintained mode, maintained mode or switching maintained mode)

is free programmable with capable emergency lighting systems. Different switching modes in one circuit are possible.

Marking: Silk-screened legend

Viewing distance: 28m

With variable wire suspension, max. 1m

Voltage range: 230 V/240V 50/60Hz, 220V DC +25/-20%

Current consumption (battery operation): 22 mA

Power consumption: 5,0 VA

Permissible temperature range: -10 °C to +40 °C

Loop terminals: 2 x 2,5 sqmm

Insulation class: I

Degree of protection: IP 41

Inclusive LED module with 18 white high brightness LEDs.

Dimensions panel (mm): 		W = 200; H = 135; T = 20

Dimensions canopy (mm): 		W = 200; H = 39; T = 46

Type: SpiritLED 16 – for surface ceiling mounting or wall parallel mounting with wire suspension

Manufactured by: CEAG

SpiritLED 16  – for surface ceiling mounting or wall mounting

Pos. ...)  ... pcs.

LED – exit sign luminaire according to DIN EN 60598-1, DIN EN 60598-2-22 and DIN EN 1838

Exclusive exit sign luminaire with LED technology with surface mounting kit. Frameless optic due to in acrylic integrated legends with LED-module. Uniform illumination of the pictogram by special lightguide technology (Lmin/max >= 0,5).

Surface mounting kit for ceiling mounting or 90° rotated wall mounting including aluminium coloured canopy.

Special LED-Converter with integrated monitoring module for individual monitoring of luminaries (monitoring of the supply and automatic detection of faulty supply of the LED-module).

Switching mode (non-maintained mode, maintained mode or switching maintained mode)

is free programmable with capable emergency lighting systems. Different switching modes in one circuit are possible.

Marking: Silk-screened legend

Viewing distance: 28m

Voltage range: 230 V/240V 50/60Hz, 220V DC +25/-20%

Current consumption (battery operation): 22 mA

Power consumption: 5,0 VA

Permissible temperature range: -10 °C to +40 °C

Loop terminals: 2 x 2,5 sqmm

Insulation class: I

Degree of protection: IP 41

Inclusive LED module with 18 white high brightness LEDs.

Dimensions panel (mm): 		W = 200, H = 147, D

Type: SpiritLED 16  – for surface ceiling mounting or wall parallel mounting with wire suspension

Manufactured by: CEAG