1903 LED CG-S

Pos.    )		pcs.

Exit sign luminaire acc. to DIN EN 60598-1, DIN EN 60598-2-22 and DIN EN 1838.

LED - exit sign luminaire for ceiling and wall mounting, with rectangular, reduced enclosure design. Lacquered plastic housing with easy mounting of the silk screend legend panel with snap-on connection. 90°-wall mounting via special 90° legends realizable.

Special LED-Converter, with integrated monitoring module for single monitoring (monitoring of the supply electronic and the LED-module). Allows single monitoring with address-switches for 20 addresses. Including easy replaceable LED-module with 3 white longlife high power LEDs on a Alucore-PCB.

Switching modes (maintained/non-maintained and switched maintained mode) freely programmable with suitable emergency lighting systems. Mixed operation possible in a single circuit.

Marking: Silk screened legend

Viewing distance: 22 m

- With double sided silk screened legend PL/PR

- With double sided silk screened legend PU/PU

- With double sided silk screened legend PU/Blind

- With double sided silk screened legend PL/PR for 90° wall mounting (Arrow to luminaire)

- With double sided silk screened legend PL/PR for 90° wall mounting (Arrow from luminaire)

Voltage range: 230 V 50/60 Hz, 220 V DC  +25/-20%

Power consumption (at 100%):  8,4VA

Power consumption (at 65%):  6,1VA

Current drawn in battery mode (at 100%): 23 mA

Current drawn in battery mode (at 65%): 17 mA

Loop terminals: 3 x 2,5 qmm

Insulation class: I, Degree of protection IP 21

Dimensions Enclosure (mm): L = 268, H = 50, D = 49

Dimensions Panel  (mm):  L = 260, H = 153, D = 20

Colour of enclosure: White / RAL 9016

Colour of enclosure: Aluminium

Accessories:

..... pcs. Mounting bracket for parallel wall mounting

Type: 1903 LED CG-S

Manufactured by: CEAG