29011 CG-S LED

Pos.    )		pcs.

Exit Luminaire acc. to EN 60598-1, EN 60598-2-22 and EN 1838.

Modular designed luminaire with one sided, rounded light exit surface, comprising: luminaire bootom and luminaire top made of 850°C glow wire resistant polycarbonate and single sided silk screened legend.

Special LED-Converter, with integrated monitoring module for single monitoring (monitoring of the supply electronic and the LED-module). Allows single monitoring with address-switches for 20 addresses. Including LED-module with 4 white superbright high power LEDs. Longer LED-life time due to an optimized power control of the LED supply.

Switching modes (maintained/non-maintained and switched maintained mode) freely programmable with suitable emergency lighting systems. Mixed operation possible in a single circuit.

Marking: Silk screened legend

Viewing distance: 32 m

Voltage range: 230 V 50/60 Hz, 220 V DC  +25/-20%

Power consumtion  (at 100%):  10,1VA

Power consumtion (at 65%):  7,5VA

Current drawn in battery mode (at 100%): 28 mA

Current drawn in battery mode (at 65%): 20 mA

Loop terminals: 3 x 2,5 qmm

Insulation class: II, Degree of protection: IP 41

Colour of enclosure: Light grey / RAL 7035

Dimensions (mm): L = 342, H = 200, D = 68

Type: 29011 LED CG-S

Manufactured by: CEAG

Pos.    )		pcs.

Accessories:

..... pcs. Wire guard

Manufactured by: CEAG

29021 CG-S LED

Pos.    )		pcs.

Exit Luminaire acc. to EN 60598-1, EN 60598-2-22 and EN 1838.

Modular designed luminaire with double sided, rounded light exit surface, comprising: of 850°C glow wire resistant polycarbonate and two sided silk screened legend.

Special LED-Converter, with integrated monitoring module for single monitoring (monitoring of the supply electronic and the LED-module). Allows single monitoring with address-switches for 20 addresses. Including LED-module with 8 white superbright high power LEDs. Longer LED-life time due to an optimized power control of the LED supply.

Switching modes (maintained/non-maintained and switched maintained mode) freely programmable with suitable emergency lighting systems. Mixed operation possible in a single circuit.

Marking: Silk screened legend

Viewing distance: 32 m

Voltage range: 230 V 50/60 Hz, 220 V DC  +25/-20%

Power consumtion  (at 100%):  16,1VA

Power consumtion (at 65%):  11,4VA

Current drawn in battery mode (at 100%): 48 mA

Current drawn in battery mode (at 65%): 34 mA

Loop terminals: 3 x 2,5 qmm

Insulation class: II, Degree of protection: IP 41

Colour of enclosure: Light grey / RAL 7035

Dimensions (mm): L = 341, H = 202, D = 92

Type: 29021 LED CG-S

Manufactured by: CEAG

Pos.    )		pcs.

Accessories

..... pcs. ceiling fixing

..... pcs. Pendulum set 0,5 m

..... pcs. Wall bracket

..... pcs. chain fixing

Manufactured by: CEAG