# 1504 LED CG-S

Pos. ...)  ... pcs.

Exit Luminaire acc. EN 60598-1, EN 60598-2-22 and EN 1838.

LED - Exit luminaire for ceiling mounting with rectangular section enclosure, 50 mm width, with easy relamping facility.

Special LED-Converter, with integrated monitoring module for single monitoring (monitoring of the supply electronic and the LED-module). Allows single monitoring with address-switches for 20 addresses. Including LED-module with 4 white superbright high power LEDs. Longer LED-life time due to an optimized power control of the LED supply.

Switching modes (maintained/non-maintained and switched emergency luminaries) freely programmable with suitable emergency lighting systems. Mixed operation possible in a single circuit.

Marking: Silk-screened legend

Viewing distance: 28 m

- With single-sided legend panel

- With double-sided legend panel

- With crystal glass panel, engraved exit legend, not accd. to DIN/EN

Voltage range: 230 V 50/60 Hz, 220 V DC  +25/-20%

Power consumtion (at 100%): 10,1VA

Power consumtion (at 65%):  7,5VA

Current drawn in battery mode (at 100%): 28 mA

Current drawn in battery mode (at 65%): 20 mA

Permissible temperature range: -10 °C up to +40 °C

Loop terminals: 3 x 2.5 sqmm

Insulation class: I, Degree of protection: IP 20

Dimensions of enclosure (mm): W = 338, H = 96, D = 75

Dimensions of panel (mm): W = 320, H = 190

Colour of enclosure:

- White, RAL 9010

Edge light for parallel to wall mounting

Type: 1504 LED CG-S

Manufactured by: CEAG

# 1604 LED CG-S

Pos. ...)  ... pcs.

Exit Luminaire acc. EN 60598-1, EN 60598-2-22 and EN 1838.

LED - Exit luminaire for ceiling mounting with rectangular section enclosure, 50 mm width, with easy relamping facility.

Special LED-Converter, with integrated monitoring module for single monitoring (monitoring of the supply electronic and the LED-module). Allows single monitoring with address-switches for 20 addresses. Including LED-module with 4 white superbright high power LEDs. Longer LED-life time due to an optimized power control of the LED supply.

Switching modes (maintained/non-maintained and switched emergency luminaries) freely programmable with suitable emergency lighting systems. Mixed operation possible in a single circuit.

Marking: Silk-screened legend

Viewing distance: 28 m

- With single-sided legend panel

- With double-sided legend panel

- With crystal glass panel, engraved exit legend, not accd. to DIN/EN

Voltage range: 230 V 50/60 Hz, 220 V DC  +25/-20%

Power consumtion (at 100%): 10,1VA

Power consumtion (at 65%):  7,5VA

Current drawn in battery mode (at 100%): 28 mA

Current drawn in battery mode (at 65%): 20 mA

Permissible temperature range: -10 °C up to +40 °C

Loop terminals: 3 x 2.5 sqmm

Insulation class: I, Degree of protection: IP 20

Dimensions of enclosure (mm): L = 430, W = 50, H = 96

Dimensions of panel (mm): W = 320, H = 190

Colour of enclosure:

- White, RAL 9010

Edge light for 90° wall mounting

Type: 1604 LED CG-S

Manufactured by: CEAG

# 1704 LED CG-S

Pos. ...)  ... pcs.

Exit Luminaire acc. EN 60598-1, EN 60598-2-22 and EN 1838.

LED - Exit luminaire for ceiling mounting with rectangular section enclosure, 50 mm width, with easy relamping facility.

Special LED-Converter, with integrated monitoring module for single monitoring (monitoring of the supply electronic and the LED-module). Allows single monitoring with address-switches for 20 addresses. Including LED-module with 4 white superbright high power LEDs. Longer LED-life time due to an optimized power control of the LED supply.

Switching modes (maintained/non-maintained and switched emergency luminaries) freely programmable with suitable emergency lighting systems. Mixed operation possible in a single circuit.

Marking: Silk-screened legend

Viewing distance: 28 m

- With single-sided legend panel

- With double-sided legend panel

- With crystal glass panel, engraved exit legend, not accd. to DIN/EN

Voltage range: 230 V 50/60 Hz, 220 V DC  +25/-20%

Power consumtion (at 100%): 10,1VA

Power consumtion (at 65%):  7,5VA

Current drawn in battery mode (at 100%): 28 mA

Current drawn in battery mode (at 65%): 20 mA

Permissible temperature range: -10 °C up to +40 °C

Loop terminals: 3 x 2.5 sqmm

Insulation class: I, Degree of protection: IP 20

Dimensions of enclosure (mm): W = 338, H = 96, D = 50

Dimensions of panel (mm): W = 320, H = 190

Colour of enclosure:

- White, RAL 9010

Ceiling mounting

Type: 1704 LED CG-S

Manufactured by: CEAG

Pos. ...)  ... pcs.

Accessories:

- Chain fastening clip incl. quick mounting set

- Pendulum set 0.5m with wall bracket/termination box, RAL 9010

- Pendulum set 1.5m with wall bracket/termination box, RAL 9010

Manufactured by: CEAG

1804 CG-S LED

Pos.    )		pcs.

Exit luminaire acc. to DIN EN 60598-1, DIN EN 60598-2-22 and DIN EN 1838.

LED-luminaire for recessed ceiling installation with plastic bezel in white colour, RAL 9010.

Special LED-Converter, with integrated monitoring module for single monitoring (monitoring of the supply electronic and the LED-module). Allows single monitoring with address-switches for 20 addresses. Including LED-module with 4 white superbright high power LEDs. Longer LED-life time due to an optimized power control of the LED supply.

Switching modes (maintained/non-maintained and switched maintained mode) freely programmable with suitable emergency lighting systems. Mixed operation possible in a single circuit.

Marking: Silk screened legend

Viewing distance: 28 m

- With single-sided legend panel

- With double-sided legend panel

Voltage range: 230 V 50/60 Hz, 220 V DC  +25/-20%

Power consumtion (at 100%): 10,1VA

Power consumtion (at 65%):  7,5VA

Current drawn in battery mode (at 100%): 28 mA

Current drawn in battery mode (at 65%): 20 mA

Permissible temperature range: -10 °C up to +40 °C

Loop terminals: 3 x 2.5 sqmm

Insulation class: I, Degree of protection: IP 20

Dimensions of panel (mm): W = 320, H = 186

Ceiling bezel (mm): L = 400, W = 100

Ceiling cut-out (mm): L = 387, W = 75

Min. mounting height (mm): 115

Type: 1804 LED CG-S

Manufactured by: CEAG

Pos.    )		pcs.

Accessories:

- Concrete mounting box for installation in concrete ceilings

- Mounting set for installation in concrete ceiling box

- metal cover in white color (RAL 9010)

Manufactured by: CEAG