RZ  70011 LED CG-S

Pos. ...)  ... pcs.

Exit Luminaire acc. EN 60598-1, EN 60598-2-22 and EN 1838.

Enclosure made of slim aluminium profile, tarnished anodized with clear cover.

Special LED-Converter, with integrated monitoring module for single monitoring (monitoring of the supply electronic and the LED-module). Allows single monitoring with address-switches for 20 addresses. Including LED-module with 2 white superbright high power LEDs. Longer LED-life time due to an optimized power control of the LED supply.

Switching modes (maintained/non-maintained and switched emergency luminaries) freely programmable with suitable emergency lighting systems. Mixed operation possible in a single circuit.

Mounting: Wall Mounting

Marking: single-sided silk screened legend

Viewing distance: 20 m

Voltage range: 230V 50/60 Hz, 220 V DC +25/-20%

Permissible temperature range: -10 °C up to +40 °C

Power consumtion  (at 100%):  5,0VA

Power consumtion (at 65%):  3,8VA

Current drawn in battery mode (at 100%): 14 mA

Current drawn in battery mode (at 65%): 10 mA

Loop terminals: 3 x 2,5 qmm

Insulation class: I, Degree of protection: IP 40

Colour of enclosure: ALU eloxiert

Dimensions (mm): L = 226, H = 125, D = 80

Type: RZ 70011 LED CG-S

Manufactured by: CEAG

Pos. ...)  ... pcs.

RZ  70021 LED WM CG-S

Pos. ...)  ... pcs.

Exit Luminaire acc. EN 60598-1, EN 60598-2-22 and EN 1838.

Enclosure made of slim aluminium profile, tarnished anodized with clear cover

Special LED-Converter, with integrated monitoring module for single monitoring (monitoring of the supply electronic and the LED-module). Allows single monitoring with address-switches for 20 addresses. Including LED-module with 4 white superbright high power LEDs. Longer LED-life time due to an optimized power control of the LED supply.

Switching modes (maintained/non-maintained and switched emergency luminaries) freely programmable with suitable emergency lighting systems. Mixed operation possible in a single circuit.

Mounting: Wall Mounting 90°

Marking: double-sided silk screened legend

Viewing distance: 20 m

Voltage range: 230V 50/60 Hz, 220 V DC +25/-20%

Permissible temperature range: -10 °C up to +40 °C

Power consumtion  (at 100%):  10,1VA

Power consumtion (at 65%):  7,5VA

Current drawn in battery mode (at 100%): 28 mA

Current drawn in battery mode (at 65%): 20 mA

Loop terminals: 3 x 2,5 qmm

Insulation class: I, Degree of protection: IP 40

Colour of enclosure: ALU eloxiert

Dimensions (mm): L = 226, H = 125, D = 80

Type: RZ 70021 LED WM CG-S

Manufactured by: CEAG

Pos. ...)  ... pcs.

Accessories:

- clear cover, structured

- Wall mounting set

Manufactured by: CEAG

# RZ  70021 LED DM CG-S

Pos. ...)  ... pcs.

Exit Luminaire acc. EN 60598-1, EN 60598-2-22 and EN 1838.

Enclosure made of slim aluminium profile, tarnished anodized with clear cover

Special LED-Converter, with integrated monitoring module for single monitoring (monitoring of the supply electronic and the LED-module). Allows single monitoring with address-switches for 20 addresses. Including LED-module with 4 white superbright high power LEDs. Longer LED-life time due to an optimized power control of the LED supply.

Switching modes (maintained/non-maintained and switched emergency luminaries) freely programmable with suitable emergency lighting systems. Mixed operation possible in a single circuit.

Mounting: Direct ceiling Mounting

Marking: double-sided silk screened legend

Viewing distance: 20 m

Voltage range: 230V 50/60 Hz, 220 V DC +25/-20%

Permissible temperature range: -10 °C up to +40 °C

Power consumtion  (at 100%):  10,1VA

Power consumtion (at 65%):  7,5VA

Current drawn in battery mode (at 100%): 28 mA

Current drawn in battery mode (at 65%): 20 mA

Loop terminals: 3 x 2,5 qmm

Insulation class: I, Degree of protection: IP 40

Colour of enclosure: ALU eloxiert

Dimensions (mm): L = 226, H = 125, D = 80

Type: RZ 70021 LED DM CG-S

Manufactured by: CEAG

Pos. ...)  ... pcs.

Accessories:

- clear cover, structured

- Ceiling mounting set 42mm

- Ceiling mounting set 100mm

- Ceiling mounting set 500mm

Manufactured by: CEAG

# RZ  70021 LED PM CG-S

Pos. ...)  ... pcs.

Exit Luminaire acc. EN 60598-1, EN 60598-2-22 and EN 1838.

Enclosure made of slim aluminium profile, tarnished anodized with clear cover

Special LED-Converter, with integrated monitoring module for single monitoring (monitoring of the supply electronic and the LED-module). Allows single monitoring with address-switches for 20 addresses. Including LED-module with 4 white superbright high power LEDs. Longer LED-life time due to an optimized power control of the LED supply.

Switching modes (maintained/non-maintained and switched emergency luminaries) freely programmable with suitable emergency lighting systems. Mixed operation possible in a single circuit.

Mounting: Pendulum Mounting

Marking: double-sided silk screened legend

Viewing distance: 20 m

Voltage range: 230V 50/60 Hz, 220 V DC +25/-20%

Permissible temperature range: -10 °C up to +40 °C

Power consumtion  (at 100%):  10,1VA

Power consumtion (at 65%):  7,5VA

Current drawn in battery mode (at 100%): 28 mA

Current drawn in battery mode (at 65%): 20 mA

Loop terminals: 3 x 2,5 qmm

Insulation class: I, Degree of protection: IP 40

Colour of enclosure: ALU eloxiert

Dimensions (mm): L = 226, H = 125, D = 80

Type: RZ 70021 LED PM CG-S

Manufactured by: CEAG

Pos. ...)  ... pcs.

Accessories:

- single pendulum 0,5m, with canopy, silver

- single pendulum 1,0m, with canopy, silver

- single pendulum 1,5m, with canopy, silver

- Chain fastening

- dummy cover

Manufactured by: CEAG