GuideLed 10021 CG-S – for ceiling installation

Pos.    )		ea.

Double-sided LED exit sign luminaire in keeping with German / European standards EN 60598-1, DIN EN 60598-2-22, DIN 4844-1 and DIN EN 1838 with surface mounting set; developed, manufactured and tested in keeping with ISO 9001.

Exit sign in LED lightguide technology for especially uniform and

bright illuminationof the pictogram:

Lm >= 500 cd/m²  of the white contrasting colour and

Lm >= 200 cd/m² across the entire pictogram

Uniformity Lmin/Lmax > 0.8.

High service life ensured by optimised LED operating conditions.

Increased safety ensured by redundant construction of the LED unit consisting of three-chip LEDs with high light efficiency > 100 lm/W for distinctly reduced connected load.

Power consumption including LED supply (apparent power / effective power):

5.5 VA / 2.9 W  	(4.0 VA / 1.9 W for PL/BL, PR/BL and PU/BL variants)

Reverse polarity protected wiring of the LED unit.

Slender design with narrow pictogram width of only 12 mm and a canopy of only 29 mm in height.

Special LED converter with integrated monitoring module for single luminaire monitoring with 20-digit address switches.

Mixed operation of the connection systems (maintained light, non-maintained light and switched maintained light within a circuit without additional data or actuating cables to the luminaires is possible in combination with suitable group or central battery systems with STAR technology.

Viewing distance:					20 m

Luminous flux at the end of the rated service time:	100%

Housing material: 					PC, PMMA

Housing colour: 					light grey RAL 7035

Connection terminal:					clamp terminal 2.5 mm²

Supply voltage:						220 - 240 VAC, 50 Hz  /  176 - 275 VDC

Current consumption - battery operation:		12 mA

(8 mA for PL/BL, PR/BL and PU/BL variants)

Class of protection:					II

Type of protection					IP 41

Permissible ambient temperature: 			-20° Celsius to +40° Celsius

Dimensions - LED pictogram (mm):			W = 226, H = 134,  D = 12

Dimensions including ceiling mounting set:  		W = 226, H = 163,  D = 42

Type: GuideLed 10021 CG-S – for ceiling installation

Make: CEAG

GuideLed 10022 CG-S – for pendant installation 0.5m

Pos.    )		ea.

Double-sided LED exit sign luminaire in keeping with German / European standards EN 60598-1, DIN EN 60598-2-22, DIN 4844-1 and DIN EN 1838 with 0.5 m pendant mounting set including canopy; developed, manufactured and tested in keeping with ISO 9001.

Exit sign in LED lightguide technology for especially uniform and

bright illuminationof the pictogram:

Lm >= 500 cd/m²  of the white contrasting colour and

Lm >= 200 cd/m² across the entire pictogram

Uniformity Lmin/Lmax > 0.8.

High service life ensured by optimised LED operating conditions.

Increased safety ensured by redundant construction of the LED unit consisting of three-chip LEDs with high light efficiency > 100 lm/W for distinctly reduced connected load.

Power consumption including LED supply (apparent power / effective power):

5.5 VA / 2.9 W  	(4.0 VA / 1.9 W for PL/BL, PR/BL and PU/BL variants)

Reverse polarity protected wiring of the LED unit.

Slender design with narrow pictogram width of only 12 mm and a canopy of only 29 mm in height.

Special LED converter with integrated monitoring module for single luminaire monitoring with 20-digit address switches.

Mixed operation of the connection systems (maintained light, non-maintained light and switched maintained light within a circuit without additional data or actuating cables to the luminaires is possible in combination with suitable group or central battery systems with STAR technology.

Viewing distance:					20 m

Luminous flux at the end of the rated service time:	100%

Housing material: 					PC, PMMA

Housing colour: 					light grey RAL 7035

Connection terminal:					clamp terminal 2.5 mm²

Supply voltage:						220 - 240 VAC, 50 Hz  /  176 - 275 VDC

Current consumption - battery operation:		12 mA

(8 mA for PL/BL, PR/BL and PU/BL variants)

Class of protection:					II

Type of protection					IP 41

Permissible ambient temperature: 			-20° Celsius to +40° Celsius

Dimensions - LED pictogram (mm):			W = 226, H = 134,  D = 12

Dimensions including ceiling mounting set:  		W = 226, H = 29,  D = 42

Type: GuideLed 10022 CG-S – for pendant installation 0.5m

Make: CEAG

GuideLed 10023 CG-S – for pendant installation 1.5m

Pos.    )		ea.

Double-sided LED exit sign luminaire in keeping with German / European standards EN 60598-1, DIN EN 60598-2-22, DIN 4844-1 and DIN EN 1838 with 1.5 m pendant mounting set including canopy; developed, manufactured and tested in keeping with ISO 9001.

Exit sign in LED lightguide technology for especially uniform and

bright illuminationof the pictogram:

Lm >= 500 cd/m²  of the white contrasting colour and

Lm >= 200 cd/m² across the entire pictogram

Uniformity Lmin/Lmax > 0.8.

High service life ensured by optimised LED operating conditions.

Increased safety ensured by redundant construction of the LED unit consisting of three-chip LEDs with high light efficiency > 100 lm/W for distinctly reduced connected load.

Power consumption including LED supply (apparent power / effective power):

5.5 VA / 2.9 W  	(4.0 VA / 1.9 W for PL/BL, PR/BL and PU/BL variants)

Reverse polarity protected wiring of the LED unit.

Slender design with narrow pictogram width of only 12 mm and a canopy of only 29 mm in height.

Special LED converter with integrated monitoring module for single luminaire monitoring with 20-digit address switches.

Mixed operation of the connection systems (maintained light, non-maintained light and switched maintained light within a circuit without additional data or actuating cables to the luminaires is possible in combination with suitable group or central battery systems with STAR technology.

Viewing distance:					20 m

Luminous flux at the end of the rated service time:	100%

Housing material: 					PC, PMMA

Housing colour: 					light grey RAL 7035

Connection terminal:					clamp terminal 2.5 mm²

Supply voltage:						220 - 240 VAC, 50 Hz  /  176 - 275 VDC

Current consumption - battery operation:		12 mA

(8 mA for PL/BL, PR/BL and PU/BL variants)

Class of protection:					II

Type of protection					IP 41

Permissible ambient temperature: 			-20° Celsius to +40° Celsius

Dimensions - LED pictogram (mm):			W = 226, H = 134,  D = 12

Dimensions including ceiling mounting set:  		W = 226, H = 29,  D = 42

Type: GuideLed 10023 CG-S – for pendant installation 1.5m

Make: CEAG

GuideLed 10024 CG-S – for recessed installation

Pos.    )		ea.

Double-sided LED exit sign luminaire in keeping with German / European standards EN 60598-1, DIN EN 60598-2-22, DIN 4844-1 and DIN EN 1838 with recessed installation set; developed, manufactured and tested in keeping with ISO 9001.

Exit sign in LED lightguide technology for especially uniform and

bright illuminationof the pictogram:

Lm >= 500 cd/m²  of the white contrasting colour and

Lm >= 200 cd/m² across the entire pictogram

Uniformity Lmin/Lmax > 0.8.

High service life ensured by optimised LED operating conditions.

Increased safety ensured by redundant construction of the LED unit consisting of three-chip LEDs with high light efficiency > 100 lm/W for distinctly reduced connected load.

Power consumption including LED supply (apparent power / effective power):

5.5 VA / 2.9 W  	(4.0 VA / 1.9 W for PL/BL, PR/BL and PU/BL variants)

Reverse polarity protected wiring of the LED unit.

Slender design with narrow pictogram width of only 12 mm and an installation depth of only 51 mm.

Ceiling installation housing made of steel sheet with continuously adjustable fastening brackets for clamping range of 1 to 30 mm.

Special LED converter with integrated monitoring module for single luminaire monitoring with 20-digit address switches.

Mixed operation of the connection systems (maintained light, non-maintained light and switched maintained light within a circuit without additional data or actuating cables to the luminaires is possible in combination with suitable group or central battery systems with STAR technology.

Viewing distance:					20 m

Luminous flux at the end of the rated service time:	100%

Housing material: 					PC, PMMA

Housing colour: 					light grey RAL 7035

Connection terminal:					clamp terminal 2.5 mm²

Supply voltage:						220 - 240 VAC, 50 Hz  /  176 - 275 VDC

Current consumption - battery operation:		12 mA

(8 mA for PL/BL, PR/BL and PU/BL variants)

Class of protection:					II

Type of protection					IP 41

Permissible ambient temperature: 			-20° Celsius to +40° Celsius

Dimensions - LED pictogram (mm):			W = 226, H = 134,  D = 12

Dimensions - mounted housing:  			W = 255, H = 51,   D = 51

Accessories:

..... ..... ea. concrete installation box including wiring set for GuideLed 10024

Type: GuideLed 10024 CG-S – for recessed installation

Make: CEAG