# SL 6011.1 CG-S

Pos. ...)  ... pcs.

Emergency Luminaire acc. EN 60598-1, EN 60598-2-22 and EN 1838.

Enclosure and structured cover made on polycarbonate.

EVG with ENEC-test mark, certified from an independent testing lab, with integrated monitoring facility. Allows single luminaire monitoring with address-switches for 20 addresses. Automatic cutout for failures within the lamp circuit.

Switching modes (maintained/non-maintained and switched emergency luminaries) freely programmable with suitable emergency lighting systems. Mixed operation possible in a single circuit.

Max. spacing between luminaire/luminaire and clear cover= 11.2 m

(mounting height = 2.5 m, C0 level, Emin = 1.25 lx, (luminous flux at the end of the rated duration)

Voltage range: 230V 50/60 Hz, 220 V DC +25/-20%

Current drawn (battery operation): 30 mA

Power consumption: 16 VA

Permissible temperature range: -10 °C up to +40 °C

Loop terminals: 3 x 2.5 sqmm

Insulation class: I; Degree of protection: IP 65

Colour of enclosure: Light grey

Inclusive lamp: 8 W T16, 450 lm

Dimensions (mm): L = 400, H = 160, D = 103

Type: SL 6011.1 CG-S

Manufactured by: CEAG

Pos. ...)  ... pcs.

Accessories:

- Wire guard

Manufactured by: CEAG

# RZ 6011.1  CG-S

Pos. ...)  ... pcs.

Exit Luminaire acc. EN 60598-1, EN 60598-2-22 and EN 1838.

Enclosure and structured cover made on poly-carbonate with three self-adhesive legend fouls PL, PR, and PU.

EVG with ENEC-test mark, certified from an independent testing lab, with integrated monitoring facility. Allows single luminaire monitoring with address-switches for 20 addresses. Automatic cutout for failures within the lamp circuit.

Switching modes (maintained/non-maintained and switched emergency luminaries) freely programmable with suitable emergency lighting systems. Mixed operation possible in a single circuit.

Marking: single-sided with legend foil

Viewing distance: 30 m

Voltage range: 230V 50/60 Hz, 220 V DC +25/-20%

Current drawn (battery operation): 30 mA

Power consumption: 16 VA

Permissible temperature range: -10 °C up to +40 °C

Loop terminals: 3 x 2.5 sqmm

Insulation class: I; Degree of protection: IP 65

Colour of enclosure: Light grey

Inclusive lamp: 8 W T16, 450 lm

Dimensions (mm): L = 400, H = 160, D = 103

Type: RZ 6011.1 CG-S

Manufactured by: CEAG

Pos. ...)  ... pcs.

Accessories:

- Wire guard

Manufactured by: CEAG