Safety luminaire 83022 CG-S

Pos.    )		pcs.

Safety luminaire with high protection class (IP65) for indoor an outdoor use in keeping with German / European standards DIN EN 60598-1, DIN EN 60598-2-22 and DIN EN 1838 for operation on safety illumination systems in keeping with German / European standards DIN VDE 0100-718, DIN EN 50172 and E DIN VDE 0108-100; developed, manufactured and tested in keeping with ISO 9001.

High impact resistant (IK08) diffuser made of UV stabilized polycarbonate for a uniform light distribution for escape route or anti panic illumination suitable for ceiling mounting as well as for wall mounting.

Maximum spacing between luminaires:

Wall mounting: 		8 m at mounting height from 2 m up to 3 m.

Ceiling mounting:      > 10 m at mounting height > 2.5m. Maximum 13.4 m at 7 m height.

(Basis for calculation: Illuminance >= 1 lx; maintenance factor = 0.8)

Robust die-cast housing in quadratic design with UV stabilized powder coating and two waterproof cable entries (IP 67) and double terminal for through wiring.

Special ECG with integrated monitoring module for single luminaire monitoring

with twenty addresses for fault and performance monitoring (CEWA GUARD technology).

Freely programmable mixed operation of the connection systems (Maintained light, non maintained light and switched maintained light) within a circuit without additional data or actuating cables to the luminaires is possible in combination with suitable safety lighting system with STAR technology.

Luminous flux at the end of the rated service time:	75 %

Housing material: 					aluminium die-cast

Housing colour: 					white, similar to RAL 9010

Connection terminal:					clamp terminal 2.5 mm²

Supply voltage:						220 - 240 VAC, 50 Hz  /  176 - 275 VDC

Connected load – mains operation:			30 VA

Current consumption - battery operation:		70 mA

Class of protection:					I

Type of protection					IP 65

Permissible ambient temperature: 			-10° Celsius to +40° Celsius

Dimensions (mm) :					L = 270, W = 270,  H = 60

Lamp type:                                                                       TC-FEL 18W

Typ: Safety luminaire 83022 CG-S

Make: CEAG

Safety luminaire 84022 CG-S

Pos.    )		pcs.

Safety luminaire with high protection class (IP65) for indoor an outdoor use in keeping with German / European standards DIN EN 60598-1, DIN EN 60598-2-22 and DIN EN 1838 for operation on safety illumination systems in keeping with German / European standards DIN VDE 0100-718, DIN EN 50172 and E DIN VDE 0108-100; developed, manufactured and tested in keeping with ISO 9001.

High impact resistant (IK08) diffuser made of UV stabilized polycarbonate for a uniform light distribution for escape route or anti panic illumination suitable for ceiling mounting as well as for wall mounting.

Maximum spacing between luminaires:

Wall mounting: 		6 m at mounting height 2.5 m.

Ceiling mounting:       > 9.3 m at mounting height > 3 m. Maximum 10.4 m at 5 m height.

(Basis for calculation: Illuminance >= 1lx; maintenance factor = 0.8)

Robust die-cast housing in round design with UV stabilized powder coating and two waterproof cable entries (IP 67) and double terminal for through wiring.

Special ECG with integrated monitoring module for single luminaire monitoring

with twenty addresses for fault and performance monitoring (CEWA GUARD technology).

Freely programmable mixed operation of the connection systems (Maintained light, non maintained light and switched maintained light) within a circuit without additional data or actuating cables to the luminaires is possible in combination with suitable safety lighting system with STAR technology.

Luminous flux at the end of the rated service time:	75 %

Housing material: 					aluminium die-cast

Housing colour: 					white, similar to RAL 9010

Connection terminal:					clamp terminal 2.5 mm²

Supply voltage:						220 - 240 VAC, 50 Hz  /  176 - 275 VDC

Connected load – mains operation:			16 VA

Current consumption - battery operation:		35 mA

Class of protection:					I

Type of protection					IP 65

Permissible ambient temperature: 			-10° Celsius to +40° Celsius

Dimensions (mm):					D = 265, H = 60

Lamp type:                                                                       TC-DEL 10W

Typ: Safety luminaire 84022 CG-S

Make: CEAG