# RZ 5001 K CG-S

Pos. ...)  ... pcs.

Cinema Exit Luminaire acc. EN 60598-1, EN 60598-2-22 and EN 1838.

With rounded enclosure outline and clear cover made of plastic. 30% luminous flux with mains operation and 100% luminous flux with battery operation, especially suitable for darkened rooms e.g. theatres or cinemas.

With integrated monitoring station, allows single luminaire monitoring with address-switches for 20 addresses.

Automatic cutout for failures within the lamp circuit. Switching modes (maintained/non-maintained and switched emergency luminaries) freely programmable with suitable emergency lighting systems. Mixed operation possible in a single circuit.

Marking: single-sided silk screened legend

Viewing distance: 17 m

Voltage range: 230V 50/60 Hz, 220 V DC +25/-20%

Current drawn (battery operation): 60 mA

Power consumption: 14 W

Permissible temperature range: -10°C up to +40°C

Loop terminals: 3 x 2.5 sqmm

Insulation class: I; Degree of protection: IP 20

Colour of enclosure: White/Silver

Inclusive lamp (tool-free replaceable): filament lamp 2 x 7 W

Dimensions (mm): L = 355, H = 100, D = 65

# Type: RZ 5001 K CG-S

Manufactured by: CEAG

Pos. ...)  ... pcs.

Accessories:

- Mounting set for wall fixing

Manufactured by: CEAG