Three-phase monitoring

..... pcs. three-phase monitoring in accordance with VDE 0108/10.89

For the monitoring of distributors for general lighting systems. For installation in the main distribution board for the general lighting system or the subdistribution board for the general lighting system including universal holder for mounting rail systems. With additional potential-free change-over contact. Trigger threshold U < 85% UN.

Colour of enclosure: red

Dimensions: B x H x D = 52.5 x 85 x 65 mm,

Pitch for 3 units

Type:	Three-phase monitoring

Manufactured by:	CEAG