# PC Software CGLine 400

# Pos. ...) ... Pcs.

PC Software CGLine 400 for Smart Media Card for configuration on PC and simple reading and processing of the test book memory.

All files can be saved for documentation on SMC and hard drive.

Printouts for Documentation:

Detailed printout of the controller configuration with the following information:

- Date and time of automatic operating duration tests incl. intervals

- Date and time of automatic function tests incl. intervals

- Relay configuration

Detailed printout of the lamp configuration per line (1 - 4) with the following information per luminaire:

- Abbreviated address (1 - 100)

- Individual name (20 characters)

- Identification number

Printouts of test book with the following options:

- Fault incident (different fault incidents can be selected separately or completely)

- Period of the test book (from – to for date and time)

- Per line or complete

- Individual comment per printout

- In the case of luminaire faults: details of individual luminaire names

... pcs. CEAG PC Software CGLine 400 for configuration and test book evaluation of the SMC

... pcs. Diskette adapter 3.5" for Smart Media Card

Type: PC Software for CGLine 400

Manufactured by: CEAG