1886- ... D CGLine

Pos.    )		Pcs.

Self-monitoring self-contained luminaire pursuant to DIN EN 60598-1, DIN EN 60598-2-22 and DIN EN 1838 for systems pursuant to DIN VDE 0108 / 10.89 for separate operation or for connection to the central monitoring device CG-Controller CGLine 400.

If connected to the central monitoring device CG-Controller CGLine 400 a non-screened 2-core bus cable to the luminaire is also needed.

Standard version with:

- Test button

- Test results with fault analysis (lamps, charging and battery circuit) as well as status displays (operation, function test, duration test) via 3 coloured LEDs

- automatic function test (weekly)

- automatic duration test (every 3 months)

- automatic charging monitoring

- deep discharge protection with restart inhibit

– no-load and short-circuit shut down of the inverter

Luminous flux (E/(N approx. 40 %

Lamp: including fluorescent tube 6 W, T16/300 Im

Emergency lighting rated operating time:

..... 1 h NC rechargeable battery 3.6 V/1.5 Ah

..... 3 h NC rechargeable battery 3.6 V/4.0 Ah

Permitted temperature range:

Maintained light: -5°C to + 30°C

Non-maintained light: 0°C to +35°C

Housing:

Edge luminaire for recessed ceiling installation including device for easy lamp changing and metal ceiling bezel in white, RAL 9010.

Insulation class: I; degree of protection: IP 20

Connection terminals: 2.5 sq mm

Supply voltage: 230V 50Hz

Panel dimensions (mm): W = 242. H = 128

Bezel dimensions (mm): L = 340. W = 100

Ceiling cut-out dimensions (mm): L = 327. W = 75

Minimum installation height (mm): 120

Panel:

- With one-sided legend panel (screen printing), viewing distance: 20m

- With two-sided legend panel (screen printing), viewing distance: 20m

- With exclusive glass panel with engraved emergency sign legend (not according to EN)

Luminaires are generally suitable for maintained or non-maintained mode.

Accessories:

..... pcs. concrete installation box for 1886

..... pcs. installation kit for concrete installation box for 1886

Type: 1886 - ... D CGLine

Manufactured by: CEAG

1888- ... D CGLine

Pos.    )		Pcs.

Self-monitoring self-contained luminaire pursuant to DIN EN 60598-1, DIN EN 60598-2-22 and DIN EN 1838 for systems pursuant to DIN VDE 0108 / 10.89 for separate operation or for connection to the central monitoring device CG-Controller CGLine 400.

If connected to the central monitoring device CG-Controller CGLine 400 a non-screened 2-core bus cable to the luminaire is also needed.

Standard version with:

- Test button

- Test results with fault analysis (lamps, charging and battery circuit) as well as status displays (operation, function test, duration test) via 3 coloured LEDs

- automatic function test (weekly)

- automatic duration test (every 3 months)

- automatic charging monitoring

- deep discharge protection with restart inhibit

– no-load and short-circuit shut down of the inverter

Luminous flux (E/(N approx. 40 %

Lamp: incl. fluorescent tube 8 W, T16/450 Im

Emergency lighting rated operating time:

..... 1 h NC rechargeable battery 3.6 V/1.5 Ah

..... 3 h NC rechargeable battery 3.6 V/4.0 Ah

Permitted temperature range:

Maintained light: -5°C to + 30°C

Non-maintained light: 0°C to +35°C

Housing:

Edge luminaire for recessed ceiling installation including device for easy lamp changing and plastic ceiling bezel in white.

Insulation class: I; degree of protection: IP 20

Connection terminals: 2.5 sq mm

Supply voltage: 230V 50Hz

Panel dimensions (mm): W = 320, H = 190

Bezel dimensions (mm): L = 400, W = 100

Ceiling cut-out dimensions (mm): L = 387, W = 75

Minimum installation height (mm): 120

Panel:

- With one-sided legend panel (screen printing), viewing distance: 28m

- With two-sided legend panel (screen printing), viewing distance: 28m

- With exclusive glass panel with engraved emergency sign legend (not according to EN)

Luminaires are generally suitable for maintained or non-maintained mode.

Accessories:

..... pcs. concrete installation box for 1888

..... pcs. installation kit for concrete installation box for 1888

Type: 1888 - ... D CGLine

Manufactured by: CEAG

1988- ... D CGLine

Pos.    )		Pcs.

Self-monitoring self-contained luminaire pursuant to DIN EN 60598-1, DIN EN 60598-2-22 and DIN EN 1838 for systems pursuant to DIN VDE 0108 / 10.89 for separate operation or for connection to the central monitoring device CG-Controller CGLine 400.

If connected to the central monitoring device CG-Controller CGLine 400 a non-screened 2-core bus cable to the luminaire is also needed.

Standard version with:

- Test button

- Test results with fault analysis (lamps, charging and battery circuit) as well as status displays (operation, function test, duration test) via 3 coloured LEDs

- automatic function test (weekly)

- automatic duration test (every 3 months)

- automatic charging monitoring

- deep discharge protection with restart inhibit

– no-load and short-circuit shut down of the inverter

Luminous flux (E/(N approx. 40 %

Lamp: incl. fluorescent tube 8 W, T16/450 Im

Emergency lighting rated operating time:

..... 1 h NC rechargeable battery 3.6 V/1.5 Ah

..... 3 h NC rechargeable battery 3.6 V/4.0 Ah

Permitted temperature range:

Maintained light: -5°C to + 30°C

Non-maintained light: 0°C to +35°C

Housing:

Edge luminaire for ceiling installation in sheet steel housing white, RAL 9010.

Insulation class: I; degree of protection: IP 20

Connection terminals: 2.5 sq mm

Supply voltage: 230V 50Hz

Panel dimensions (mm): W = 320. H = 190

Housing dimensions (mm): L = 361. H = 120. D = 86

Panel:

- With one-sided legend panel (screen printing), viewing distance: 28m

- With two-sided legend panel (screen printing), viewing distance: 28m

- With exclusive glass panel with engraved emergency sign legend (not according to EN)

Luminaires are generally suitable for maintained or non-maintained mode.

Accessories:

..... pcs. pair of pendants 0.5 m

..... pcs. bracket

..... pcs. parallel wall fixing

..... pcs. chain fixing

Type: 1988 - ... D CGLine

Manufactured by: CEAG