W276.3/4

___ pcs. handheld torch with emergency lighting function acc. to VDE 0108 dated 10.89 and EN 60598 part 2.22 and built-in charging unit. The luminaries comply with the EMC requirements acc. to directive 89/336/EEC. With monitoring of the charging circuit and function indication by means of green LED.

Enclosure made of impact resistant, abrasion-resistant plastic.

Colour of enclosure: grey

Including slip-on filter set: 
red, orange, clear prismatic

Duration of emergency lighting:
– 3.5 h with incandescent lamp 5V/5W 
   (main beam)

– 12.0 h with incandescent lamp 4.8V/5W
   (auxiliary beam)

Battery: rechargeable, maintenance-free and gas-tight NC rechargeable battery 4.8V/4Ah

Voltage: 230V, 50/60Hz, 10VA

Insulation class: II, Degree of protection: IP54

Switching function: 
flashing light, maintained light and auxiliary light

Illumination: 
5 m 256 Lux, 20m 16 Lux, 80m 1 Lux

Connection cable: 
spiral cable with Euro connector

Options

h Shock-tested wall bracket

h Wall console

Type: W276.3/4

Manufactured by: CEAG