W270.3/4

___ pcs. handheld torch with emergency lighting function acc. to VDE 0108 dated 10.89 and EN 60598 part 2.22. The luminaries comply with the EMC requirements acc. to directive 89/336/EEC. With monitoring of the charging circuit and function indication by means of green LED.

Enclosure made of impact resistant, abrasion-resistant plastic.

Colour of enclosure: grey

Including slip-on filter set: 
red, orange, clear prismatic

Duration of emergency lighting:
– 3.5 h with incandescent lamp 5V/5W 
   (main beam)

– 12.0 h with incandescent lamp 4.8V/5W
   (auxiliary beam)

Battery: rechargeable, maintenance-free and gas-tight NC rechargeable battery 4.8V/4Ah

Insulation class: II, Degree of protection: IP54

Switching function: 
flashing light, maintained light and auxiliary light

Illumination: 
5 m 256 Lux, 20m 16 Lux, 80m 1 Lux

Rechargeable in charging unit Z345.3

Type: W270.3/4

Manufactured by: CEAG

W270.3/7

___ pcs. handheld torch with emergency lighting function acc. to VDE 0108 dated 10.89 and EN 60598 part 2.22. The luminaries comply with the EMC requirements acc. to directive 89/336/EEC. With monitoring of the charging circuit and function indication by means of green LED.

Enclosure made of impact resistant, abrasion-resistant plastic.

Colour of enclosure: grey

Including slip-on filter set: 
red, orange, clear prismatic

Duration of emergency lighting:
– 6.5 h with incandescent lamp 5V/5W 
   (main beam)

– 25.0 h with incandescent lamp 4.8V/5W
   (auxiliary beam)

Battery: rechargeable, maintenance-free and gas-tight NC rechargeable battery 4.8V/7Ah

Insulation class: II, Degree of protection: IP54

Switching function: 
flashing light, maintained light and auxiliary light

Illumination: 
5 m 256 Lux, 20m 16 Lux, 80m 1 Lux

Rechargeable in charging unit Z345.3

Type: W270.3/7

Manufactured by: CEAG

Z345.3

___ pcs. charging unit for handheld torch W276.3. The charging unit complies with the EMC requirements acc. to directive 89/336/EEC.

Enclosure material: impact resistant, abrasion-resistant plastic

Colour of enclosure: grey

Voltage: 230 V, 50/60 Hz, 10 VA

Insulation class: II, Degree of protection: IP54

Type:	Z345.3

Manufactured by: CEAG