SEB 8 L

___ pcs. Explosion protected handheld torch acc. to EN 50014ff with emergency lighting function acc. to VDE 0108 dated 10.89 and EN 60598 part 2.22 and built-in charging unit. The luminaires comply with the EMC require-ments acc. to directive 89/336/EEC.

–	Electronic operating time display

–	Charge depending on drawn capacity

–	Flashlight

–	Emergency light in case of mains failure

–	Automatic switchover to pilot light in case
	reserve or broken filament

Explosion category: 
EEx e ib IIC T4 for zone 1 and 2

EC-Type Examination Certificate: PTB 99 ATEX 2195

With monitoring of the charging circuit and function indication by means of 5 LEDs. Enclosure made of polyamide.

Colour of enclosure: black

Light aperture: 98 mm, mineral glass

Focussing beam, including slip-on filter set: Red, orange, clear prismatic

Lamp main beam: 
Halogen lamp with double bulb 5.5V/5.5W

Lamp pilot light: tungsten lamp 4.8V/0.3A

Duration of emergency lighting: 	
6.5 h with lamp 5.5V/5.5W (main beam)

12.0 h with lamp 4.8V/0.3A (pilot light)

Battery: rechargeable, maintainance-free and gas tight NC battery 4.8V/7Ah

Voltage: 230V 50/60 Hz, 14VA

Insulation class: II (battery operation = III)

Degree of protection: IP65

Switching function: 
Flashing light, maintained light and auxiliary light

Illumination: 
20 m 49 Lux, 80 m 3 Lux, 150 m 1 Lux

Chargeable via integrated mains lead or optional motor vehicle charging unit 90.

Type:	SEB 8 L

Manufactured by:	CEAG

SEB 8

___ pcs. Explosion protected handheld torch acc. to EN 50014ff with emergency lighting function acc. to VDE 0108 dated 10.89 and EN 60598 part 2.22 and built-in charging unit. The luminaires comply with the EMC require-ments acc. to directive 89/336/EEC.

–	Electronic operating time display

–	Charge depending on drawn capacity

–	Flashlight

–	Emergency light in case of mains failure

–	Automatic switchover to pilot light in case
	reserve or broken filament

Explosion category: 
EEx e ib IIC T4 for zone 1 and 2

EC-Type Examination Certificate: 
PTB 99 ATEX 2195

With monitoring of the charging circuit and function indication by means of 5 LEDs. Enclosure made of polyamide.

Colour of enclosure: black

Light aperture: 98 mm, mineral glass

Focussing beam, including slip-on filter set: 
Red, orange, clear prismatic

Lamp main beam: 
Halogen lamp with double bulb 5.5V/5.5W

Lamp pilot light: tungsten lamp 4.8V/0.3A

Duration of emergency lighting: 	
6.5 h with lamp 5.5V/5.5W (main beam)

12.0 h with lamp 4.8V/0.3A (pilot light)

Battery: rechargeable, maintainance-free and gas tight NC battery 4.8V/7Ah

Voltage: 230V 50/60 Hz, 14VA

Insulation class: II (battery operation = III)

Degree of protection: IP65

Switching function: 
Flashing light, maintained light and auxiliary light

Illumination: 
5 m 256 Lux, 80 m 3 Lux, 150 m 1 Lux

Chargeable via charging unit LG 443 or motor vehicle charging unit 90.

Type:	SEB 8

Manufactured by:	CEAG