Pos.    )		... pcs.

EVG 13.3 V-CG-S

High frequency electronic ballast acc. to EN 60929, EN 61347-2-3 and EN 61347-2-4 for a 4-pin fluorescent lamp 4 – 13 W with 20 addresses for function monitoring (CEWA GUARD Technology) in DC-operation without additional data line.

Inclusive automatic cut-out for failures within the lamp circuit.

Suitable to be mounted in luminaires of insulation class I or II for emergency luminaires acc. to EN 60598-2-22 and for the operation in emergency lighting systems acc. to DIN VDE 0100-718, DIN EN 50172 and E DIN VDE 0108-100.

Acc. to ISO 9001 developed, manufactured and tested.

With ENEC-compliance, certified by an independent testing laboratory.

Switching modes (maintained/non-maintained and switched emergency luminaires) freely programmable in one circuit without additional data line to the luminaires in conjunction with suitable emergency lighting systems (with STAR-Technology).

Voltage:			220 – 240 V, 50/60 Hz /176 – 275 V DC

Standby power loss:		< 0.5 W (230 V / 50 Hz)

Lamp load:			4-pin fluorescent lamp 4 – 13 W

Max. distance

Luminaire / EVG:		1 m

Degree of protection:		IP 20

Permissible

Temperature range ta:		-20°C to +60°C

Max. permissible

Test point temperature tc:	75°C

Connection terminals:		plug terminals 2.5 mm², mains connection reverse polarity protection

Dimensions (mm): 		H = 27.5; L = 140; W = 39

Fitting position:			horizontal

Enclosure material:		flame-retardant polycarbonate

Luminous flux (E / (N at the

end of the operating time:	75%

Type: EVG 13.3 V-CG-S

Manufactured by: CEAG