CGVision

Pos.   )		pcs.

CG Vision – fully automatic visualisation-, monitoring- and programming software for usual pc`s with Windows 2000™ or Windows XP™- system software acc. to VDE 0108/10.89 By CG-S Bus technology detailed system information is available at any time.

- simple menu guidance

- complete visualisation, monitoring and programming of systems with STAR-

technology at only one bus line

- up to 480 emergency lighting devices are monitor- and programmable, a segmentation in up to 15

groups of devices is possible (one device group per device family)

- external LON-switches on luminaries and circuits in systems with STAR-technology are
  programmable

- free input of texts for i.e. location marking (up to 20 signs)
– operator program under Windows 2000™ or Windows XP™- system software

- inquiry of the current working conditions of all mounted systems

- constant display of the 4 latest events

- localised failure display about each emergency circuit and SL/RZ luminaries with destination data

in plain text in connection with function tests

- always current information on charging unit and battery

- storage and retrieval possibility of all log book entries over a period of 2 years at least

- additional storage of the data on external data carrier is possible at each time

- free programmable function- and duration test 
- the functions are compatible with EGA-technology (available as software amplification, optional)

Options:

.... pcs.: PC-amplification software for the visualisation of a CEAG EGA-line for ZB96 on

CG Vision

.... pcs:  EGA/RS 232-Interface

Type: PC-software CGVision basic version

Manufactured by: CEAG