EGA / PC – Interface - 2

Pos.   )		pcs.

EGA / PC – Interface –2 for operation of CEAG emergency lighting systems with EGA-bus technology, with up to two data lines via EGA bus, on CGVision visualisation-, monitoring- and programming software.

The interface is designed to connect to a standard PC with Windows XP™ or Windows 2000™ via RS232-interface (COM-Port).

It is possible to connect up to 32 EGA-emergency lighting systems each line. An external power supply 24V/1,5A is necessary.

Supply voltage:	24V/DC

Power consumption: 	max. 400mA each line, depending of the no. of connected systems

Connector EGA:	screw terminal, pluggable, max. 2,5 qmm

Connector PC:	2 x DB9 (COM-Port)

Housing type: 	Din rail housing with 7TE

Dimensions:	L=126mm, W=122,5mm, H=64mm

Weight: 	approx. 400g

Degree od protection: 	IP20

LED-display (each line): 	1 x 24V (yellow), 1 x 5V (yellow), 1 x Data Out (green), 1 x Data In (red)

Type: EGA / PC – Interface - 2

Manufactured by: CEAG