EGA/RS 232-Interface

Pos.   )		 pcs.

EGA/RS 232-Interface

EGA–Interface Box for the operation of CEAG emergency lighting systems of one line via EGA-Bus with CGVision visualisation-, monitoring- and programming-software.

The connection occurs by a RS 232-port (COM-Port) at usual pc`s with Windows 2000™ Windows XP™- system software. The supply occurs with 230V/AC appliance plug.

Power Supply:	 		230V/AC

Build-up housing:		polycarbonate

Dimensions: 			L=150mm, W=82mm, H=45mm

Weight: approx. 		400g

Degree of protection: 		IP20

Connections: 			1 x RS 232 (DB9), 1 x EGA (3-core), 1 x 230V/AC

LED-Display: 	1 x 24V (yellow), 1 x 5V (yellow), 1 x Data Out (green), 
1 x Data In (red)

Type: EGA/RS 232-Interface

Manufactured by: CEAG