CG-S Bus 2-Way Repeater

Pos.   )		pcs.

2-Way Repeater to connect CG-S Bus networks and to increase the extension of the net of a CG-S Bus network by a physical split into two CG-S Bus networks.

With an extension of more than two CG-S networks repeater and router must be planned alternately.

Functions:

- to build CG-S network segments

- to increase the net extension

Operation voltage : 		24V AC/DC

Power consumption: 		< 1W

Housing of polycarbonate:	for DIN-rail mounting

Dimensions: 			L=105 mm, W=86 mm, H=58 mm

Weight: 			approx. 200 g

Degree of protection: 		IP20

A separately available mains adapter 220V AC/DC; 24V DC for mains supply is necessary

Type: CG-S Bus 2-Way Repeater

Manufactured by: CEAG