CG-S Bus Router

Pos.   )		pcs.

Router to connect CG-S Bus networks and to increase the extension of the net of a CG-S Bus network by logical and physical structuring with signal refreshing function of the CG-S Bus.

Functions:

- Signal amplification and regeneration

- Establishment of CG-S network segments

- Elimination of interferences

- Increase the net extension

- Logical filter function

- Diagnostic function

Operation voltage: 		24V AC/DC

Power consumption: 		< 1W

Housing of polycarbonate:	for DIN-rail mounting

Dimensions: 			L=105 mm, W=86 mm, H=58 mm

Weight: approx. 		200 g

Degree of protection: 		IP20

A separately available mains adapter 220V AC/DC; 24V DC for mains supply is necessary

Type: CG-S Bus Router

Manufactured by: CEAG