CG-S/IP-Router

Pos.   )		pcs.

CG-S/IP Router to connect CEAG emergency lighting systems with CG-S Bus at CGVision via at site existing Ethernet (with TCP/IP).

Simple, even building-spanned connection of peripheraly placed CEAG emergency lighting systems with STAR-technology by linking CG-S/IP-Router which are configured as clients via Ethernet. The connection to the CGVision occurs by a G-S/IP-Router which is configured as configuration server.

CG-S/IP Router:

- Clients DHCP able

- Integrated configuration server

- Network diagnosis-LEDs

- Integrated web server for the configuration

- Real time watch with battery buffering

Operation voltage: 		24V AC/DC

Power consumption: 		< 1W

Plastic housing:			for DIN-rail mounting

Dimensions: 			L=157 mm, W=86 mm, H=60 mm

Degree of protection: 		IP20

A separately available mains adapter 220V AC/DC; 24V DC for mains supply is necessary

Type: CG-S/IP-Router

Manufactured by: CEAG