Mains adapter 230V AC/DC, 24V DC

Pos.   )		 pcs.

Electronic mains adapter for 230V AC/DC supply. For the supply of CEAG network components (Router, 2-Way-Repeater etc.) with usual mains feed with 230V AC or by a final circuit with 230V AC respectively 220V DC with battery operation, to ensure the function of the network components even with mains failure.

Supply voltage type.: 			230V AC/DC

Supply voltage ambient:			85...264 VAC, 90...300V DC

Frequency :				0/47-63 Hz

Output voltage:				24V DC +/- 3%

Output current max.:			1A

Housing:				for DIN-rail mounting

Dimensions: 				W=43,5 mm, H=88,5 mm, D=115 mm

Weight: 				approx. 220 g

Insulation class: 			IP20

Type: Mains adapter 230V AC/DC, 24V DC

Manufactured by: CEAG