Webmodul ZB-S

Webmodul ZB-S for visualisation and monitoring of a central battery system, Type ZB-S via a local ethernet (LAN) or internet (WWW) with a usual WEB-Browser. An access to the webmodule via internet (WWW) must be administrated from an IT-department at site!

Integrated mail-client for a comfortable, event orientated failure information, for up to 5 E-mail recipients. Access via administrator account or guest account, with password protection.

- Easy menu structure

- Full visualisation and monitoring of a ZB-S (central battery system) via ethernet (LAN) with usual

WEB-Browser (e.g. Internet Explorer, Firefox etc.)

- Display of all actual operation modes

- Local failure information of each emergency circuit and luminaires with destination information in

plain text

- Permanent actual information of the charging unit and the battery

- Parallel access to the webmodule from different workstations possible (max. 8)

- Integrated mail-client for comfortable failure notification via mail

- Type of different failures for the mail transmission selectable

- Up to 5 mail-recipients programmable

- Actualisation cycle of the web browser via the webmodule adjustable

- Authenticated access via administrator-account with password protection

- Adjustable guest account with restricted access with password protection

- Static or dynamic (DHCP) IP-addressing possible

Supply voltage: 24V DC

Power consumption: < 1,5W

LAN connection: RJ45

Housing: Polycarbonat for DIN-rail mounting, 2TE

Dimmensions: L=90 mm, W=35 mm, H=58 mm

Weight: approx. 100 g

Degree of protection: IP20

Type: Webmodul ZB-S

Manufacturer: CEAG