# CG-Controller ZB-S

# Pos. ...)  ... pcs.

Microcomputer-based controller for the control and monitoring of max. 32 devices or sub-stations. All data and commands are passed over CG-S data bus. Plastic enclosure with viewing door, cable feed-through above or behind.

Functions:

- Start function test, test interval can be selected as required

- Start operating time test, test interval can be selected as required

- Cancel operating time test

- Continuous device status monitoring

- Recording the individual error messages

- Interrogation of the current fit

- Freely programmable potential-free contact for charging failure, luminaire failure, insulation fault, mains failure or battery operation.

- Display output in plain text, display with background lighting

- LED indicators: operation, test and failure

- Alphanumeric keypad for programming and entering text on the controller

- Removable configuration and log book memory (SD-card) with data retention for a period of at least 2 years

- Evaluation of the log book (memory card) on commercially available PC using optional card reader and CEAG software

- Pre-programming of the configuration memory on the PC

- Entry of luminaire location data of 20 characters each on memory card using the PC

With universal holder for mounting rail systems or wall mounting

Dimensions (mm): H = 184, W = 240, D = 112

Connection terminals: 2.5 sqmm

Voltage : 230 V AC or 24 V DC

Degree of protection: IP 65

Colour: RAL 7035

Options:

..... pcs. CEAG- memory card, formatted for the use in the CG-Controller ZB-S

..... pcs. card reader for memory cards

..... pcs. CEAG PC software for pre-programming the memory card for the CG-Controller ZB-S

Type: CG-Controller ZB-S

Manufactured by: CEAG