# F3 remote indication

# Pos. ...)  ... pcs.

F3 remote indication complies DIN VDE 0100-718

For the remote indication of the operating states of the central battery system. Function is also ensured in case of mains failure. It is possible to block emergency lighting operation using a key-operated switch. The uphold battery charge is not effect by blocking of the emergency operation.

On a short circuit or wire recognition the differential loop control puts the system into the non-maintained modus.

LED indicators: system operation, battery operation, system failure.

Enclosure: plastic enclosure for surface mounting

Dimensions (mm): W = 80, H = 160, D = 55

Connection terminals: 2.5 sqmm rigid and flexible

Type: F3 remote indication

Supplier: CEAG

# F3 remote indication flush-mounted

# Pos. ...)  ... pcs.

F3 remote indication complies DIN VDE 0100-718

For the remote indication of the operating states of the central battery system. Function is also ensured in case of mains failure. It is possible to block emergency lighting operation using a key-operated switch. The uphold battery charge is not effect by blocking of the emergency operation.

On a short circuit or wire recognition the differential loop control puts the system into the non-maintained modus.

LED indicators: system operation, battery operation, system failure.

Performance for installation in the flush-mounted switch receptively empty space box acc. DIN VDE 0606

Connection terminals: 1.5 sqmm rigid or 1.0 sqmm flexible

Colour of the front panel is similar to RAL7035 light grey

Type: F3 remote indication flush-mounted

Supplier: CEAG