External TLS-Bus-Module

# Pos. ...)  ... pcs.

..... off External TLS Bus Module

For polling stairwell light pushbuttons and supplying glow lamps during emergency operation. General and safety luminaires can be controlled with the same pushbuttons by using a TLS switching module (installed in the lighting distribution system)

2 pushbutton inputs (2.5 sqmm) including supply of glow lamps, max. 50 mA per TLS input.

2 load circuits for general lighting (2.5 sqmm), max. 10 A per circuit (120 A/ms).

Variable 'on' time ranging from 1 to 15 minutes, including glow lamp flash function 30 s before the end of the preset on time.

Connection of RS 485 bus, 24 V module power supply and supply cable from final circuit for the generation of the glow lamp voltage.

Addressable by decode switch, LEDs for Fault, ON status and Run.

Enclosure for DIN rail mounting.

Dimensions: h = 60 mm, w = 85 mm, l = 105 mm.

User-programmable assignment of independent TLS inputs for each emergency light circuit or luminaire as well as individual name per bus-module in the control module.

Type: TLS-Bus Module

Supplier: CEAG