# External DLS/3Ph-Bus-Module

# Pos. ...)  ... pcs.

..... off External DLS/3Ph Bus Module complies DIN VDE 0100-718 for installation in sub-distribution boards for the general lighting.

Suitable for use as a phase monitor and for light switch polling (DLS) for the common switching of safety and general lighting systems. An additional data cable to the luminaires is not required.

8 DLS inputs (2.5 sqmm) with LED indicators or 5 DLS inputs combined with 3 phase monitor inputs can be activated by a selector switch.

Monitoring thresholds as per DIN VDE 0100-718.

Connection of RS485 bus and 24 V module supply.

Addressable by decode switch, LEDs for Fault, ON status and Run.

Enclosure for DIN rail mounting.

Dimensions: h = 60 mm, w = 85 mm, l = 105 mm.

User-programmable assignment of independent DLS inputs for each emergency light circuit or luminaire as well as individual name per bus-module in the control module.

When using as a 3 phase monitor the detailed phase failure information with location of the mains distribution board will be displayed in the control module.

Type: DLS/3PH Bus Module

Supplier: CEAG

# External DLS/3Ph-Bus-Module inverse

# Pos. ...)  ... pcs.

..... off External DLS/3Ph Bus Module complies DIN VDE 0100-718 with inverse switching logic for installation in sub-distribution boards for the general lighting.

Suitable for use as a phase monitor and for light switch polling (DLS) with inverse switching logic for the common switching of safety and general lighting systems or for the control of the circuit-breaker.

An additional data cable to the luminaires is not required.

8 DLS inputs inverse (2.5 sqmm) with LED indicators or 5 DLS inputs inverse combined with 3 phase monitor inputs can be activated by a selector switch.

Monitoring thresholds as per DIN VDE 0100-718

Connection of RS485 bus and 24 V module supply.

Addressable by decode switch, LEDs for Fault, ON status and Run.

Enclosure for DIN rail mounting.

Dimensions: h = 60 mm, w = 85 mm, l = 105 mm.

User-programmable assignment of independent DLS inputs for each emergency light circuit or luminaire as well as individual name per bus-module in the control module.

When using as a 3 phase monitor the detailed phase failure information with location of the mains distribution board will be displayed in the control module.

Type: DLS/3PH Bus Module inverse

Supplier: CEAG