# CG-Controller ZB96

# Pos. ...)  ... pcs.

CG-Controller ZB96 acc. VDE 0108 10/89.

Microcomputer-based controller for the control and monitoring of max. 32 devices or sub-stations. All data and commands are passed over a three-wire serial data bus. Plastic enclosure with viewing door, cable feed-through above or behind.

Functions:

- Start function test, test interval can be selected as required

- Start operating time test, test interval can be selected as required

- Cancel operating time test

- Continuous device status monitoring

- Recording the individual error messages

- Interrogation of the current fit

- Freely programmable potential-free contact for charging failure, luminaire failure, insulation fault, mains failure or battery operation.

- Display output in plain text, display with background lighting

- LED indicators: operation, test and failure

- Alphanumeric keypad for programming and entering text on the controller

- Removable configuration and log book memory (smart media card) with data retention for a period of at least 2 years

- Evaluation of the log book (smart media card) on commercially available PC using optional adapter floppy disk and CEAG software

- Pre-programming of the configuration memory on the PC

- Entry of luminaire location data of 20 characters each on smart media card using the PC

With universal holder for mounting rail systems or wall mounting

Dimensions (mm): H = 184, W = 240, D = 112

Connection terminals: 2.5 sqmm, 2 x 2.56 mm for data cables

Voltage : 230 V AC or 24 V DC

Degree of protection: IP 65

Colour: RAL 7035

Options:

..... pcs. CEAG-Smart-Media memory card, formatted for the use in the CG-Controller ZB96

..... pcs. smart media adapter disk 3.5”

..... pcs. CEAG PC software for pre-programming the smart media card for the CG-Controller ZB96

Type: CG-Controller ZB96

Manufactured by: CEAG

PC programming software for CG Controller ZB96

# Pos. ...)  ... pcs.

Programming software for CEAG Smart-Media-Card of the CG Controller ZB96 for the quick pre-programming at the PC and simply reading and editing of the logbook.

...... off CEAG PC software “CG Controller ZB96” for external programming of SMC via PC

...... off diskette adapter 3.5" for smart media card

Type: PC programming software for CG Controller ZB96

Supplier: CEAG