CG controller CG 2000

Microcomputer-based controller for the control and monitoring of max. 32 devices or sub-stations. All data and commands are passed over a separate data bus.

Plastic enclosure with viewing door, cable feed-through above or behind.

Functions:

•	Start function test, test interval can be selected as required

•	Start operating time test, test interval can be selected as required

•	Cancel operating time test

•	Continuous device status monitoring

•	Recording the individual error messages

•	Interrogation of the current fit

•	Freely programmable potential-free contact for charging failure, luminaire failure, insulation fault, mains failure or battery operation.

•	Display output in plain text, display with background lighting

•	LED indicators: power, test and failure

•	Alphanumeric keypad for programming and entering text on the controller

•	Removable configuration and log book memory (memory card) with data retention for a period of at least 2 years

•	Evaluation of the log book (memory card) using optional adapter floppy disk and CEAG software on commercially available PC

•	Pre-programming of the configuration memory on the PC

•	Entry of up to 6400 items of luminaire location data of 20 characters each on smart media card on the PC

With universal holder for mounting rail systems or wall mounting

Dimensions (mm): H=184mm, B=240, D=112

Connection terminals: 2.5 mm2, 2 x 2.5 mm for data cables

Voltage : 230V AC or 24V DC

Degree of protection: IP65

Colour: RAL 7035

Options:

.... pcs. memory card, formatted

.... pcs. card reader for memory cards

.... pcs. CEAG PC software for programming the memory card for the CG controller CG 2000

Type:	CG controller

Manufactured by:	CEAG