External TLS-BUS-module

.... pcs. external TLS module for monitoring staircase light buttons and supplying glow lamps during emergency operation.

•	Enclosure for DIN rail mounting.

•	2 button inputs (2.5 mm2) including supply of glow lamps (max. 50 mA) and control of 2 switched outputs 230 V 10 A (120 A/ms)

•	Glow lamp flashing function prior to expiry of the time delay set (30 s before expiry)

•	Connection of RS 485 bus, 24V module power supply and supply cable from final circuit for the generation of the glow lamp voltage.

•	Dimensions (B x H x D/mm): 105 x 60 x 85

Type: TLS-BUS-module external

Manufactured by:	CEAG